## Slide 1
Cosmos3-Edge on
Jetson Orin Nano
Public implementation and measured findings
Selected configuration: fp16-corrected-i1024-kv2048
2026-09-20
Notes: Original presentation design. A final label requires explicit selected-candidate and completed-soak evidence.
Measured values supplied by output/final-findings-data.json.
Sources:
results/optimization-selection.json
results/raw/soak-final-service-01.summary.json

## Slide 2
Installed hardware and software
Measured findings, 2026-09-20
2
Component | Observed configuration
Device | Jetson Orin Nano P3767-0005 8 GB shared RAM
Storage and mode | WD_BLACK SN7100 1 TB Stock 25 W, ID1
Operating system | JetPack 7.2.1, L4T 39.2.1 Kernel 6.8.12-1021-tegra
Compute libraries | CUDA nvcc13.2.86, TensorRT 10.16.2.10
Installation evidence | Verified USB-C QSPI + NVMe flash Verified NVMe boot and CUDA calculation
Official NVIDIA flash tools ran through an original SSH/NFS transport bridge.
Notes: Installed platform facts come from the actual device receipts. Advertised RAM and Linux MemTotal are distinct.
Measured values supplied by output/final-findings-data.json.
Sources:
results/normal-boot.json
results/jetpack-flash-status.json
results/installed-compute-packages.json
https://developer.nvidia.com/embedded/jetpack/downloads

## Slide 3
Streaming browser interface
Measured findings, 2026-09-20
3
Browser checks
Streaming: Pass
Stop and restart: Pass
Synthetic camera: Pass
Web access
http://localhost:8090
Actual Orin service through the Mac SSH tunnel
Notes: Original UI and actual inference screenshot. Crop removes lower settings only. Screenshot timing is one request, not the benchmark distribution. The screenshot does not establish general image accuracy.
Measured values supplied by output/final-findings-data.json.
Sources:
results/browser-live-ui-final.json
results/browser-live-ui-final.json
results/browser-camera-ui-final.json
https://github.com/NVIDIA-AI-IOT/live-vlm-webui

## Slide 4
Request and inference path
Measured findings, 2026-09-20
4
Stage | Responsibility | Source
Browser | Capture JPEG, prompt and sampling settings | Original UI
Orin HTTP proxy | Forward one request and stream SSE events | Original proxy
Resident backend | Decode image, run vision and language engines | TensorRT Edge-LLM
Checkpoint | Learned image and language behavior | NVIDIA Cosmos3-Edge
Browser response | Incremental text, timing and cancellation | Original UI
The webpage runs on the Orin. Access through a tunnel remains a transport detail.
Notes: Original browser/proxy components wrap the public TensorRT Edge-LLM reasoner. One active request prevents accumulating frames. The application displays only real upstream token deltas.
Measured values supplied by output/final-findings-data.json.
Sources:
scripts/serve_ui.py
web/app.js
https://github.com/NVIDIA/TensorRT-Edge-LLM/blob/e8b29522938901f6df19ebeedd4b69bc8edbcd97/experimental/server/cli.py
https://github.com/NVIDIA/TensorRT-Edge-LLM/blob/e8b29522938901f6df19ebeedd4b69bc8edbcd97/experimental/server/runtime/engine.py

## Slide 5
Compatibility and correctness repairs
Measured findings, 2026-09-20
5
Observed defect | Task contribution using public conventions
Generated runtime sidecars | Restore existing RoPE aliases and image/video delimiters
HWC weights with CHW pixels | Apply the public exporter’s patch-weight column permutation
Position interpolation | Select the Cosmos half-pixel convention in the existing kernel
Independent image cache | Expose its existing byte budget and set it to zero for measurement
NVIDIA supplies the model, runtime and underlying conventions. This task repairs their integration.
Notes: These original diagnoses and small integrations reuse the public model/exporter conventions. No model training or new interpolation algorithm is claimed. Patch projection requires a fresh visual engine. Position and cache API changes require rebuilding the native binding.
Measured values supplied by output/final-findings-data.json.
Sources:
patches/cosmos3-patch-embedding-chw.md
patches/cosmos3-half-pixel-position.md
patches/encoder-cache-budget.json
scripts/repair_cosmos_runtime_config.py
scripts/repair_cosmos_chat_template.py
https://github.com/NVIDIA/TensorRT-Edge-LLM/blob/e8b29522938901f6df19ebeedd4b69bc8edbcd97/tensorrt_edgellm/models/cosmos3_reasoner/modeling_cosmos3_reasoner_visual.py
https://github.com/huggingface/transformers/blob/c587bc884db2c2e31fc2b8102314656b17aa07b1/src/transformers/models/cosmos3_edge/modeling_cosmos3_edge.py

## Slide 6
Quality checks and their limits
Measured findings, 2026-09-20
6
Natural photos
5/9 with partial credit.
0/3 fully correct photos.
Official reference also 5/9.
2/3 answers match exactly.
Cause remains unassigned.
18 / 19 synthetic facts
Strict screen: Fail
Reference equivalence: Accepted
Both paths describe the flat circles as spheres.
Official answer identical: Yes
All previously correct facts must remain correct. No additional false claim is permitted.
Notes: Strict six-image fixture grading and optimization equivalence are separate. The official unmodified model reproduced the entire case05 sphere answer on the exact image and prompt. A pre-INT4 policy preserves every previously correct fact and permits only that precise known error. It does not turn the strict 18/19 result into a 19/19 pass.
The distinct natural-photo smoke check is outside candidate selection. Fully correct photos means every required observation is correct, not merely a completed HTTP response. The natural-image official reference runs the unchanged public model through Transformers on Mac MPS FP16. It scores 5/9 with the same grading interpretation, with 2/3 answers exactly matching the Orin. In the recorded comparison, market gives only "Carrots." and dog incorrectly says "wooden deck" in both paths. The cap/mitt wording differs but both miss the required cap-on-mitt relation. The displayed 5/9 gives generous partial credit for carrot identity even though "Carrots." omits the required lower-right relation. Strict full-fact grading is 4/9. No photo satisfies every required fact under either interpretation. These observations do not establish a model-only cause for every failure. Mac execution time is diagnostic and is not an Orin performance measurement.
Captured official reference answer: Both objects are purple. The left object, which is a sphere, is larger than the right object, which is a smaller sphere.
Measured values supplied by output/final-findings-data.json.
Sources:
results/quality-final-service-01-review.json
results/optimization-quality-policy.json
results/reference-official-05-comparison.json
results/natural-smoke-final-01-review.json
results/reference-natural-smoke.json
benchmarks/natural-smoke/manifest.json
benchmarks/natural-smoke/README.md
results/reference-official-05.json
https://huggingface.co/nvidia/Cosmos3-Edge/blob/344d602b128d1bbdacb43b08d0a3626f46343e29/README.md

## Slide 7
Measurement workload and stopping rule
Measured findings, 2026-09-20
7
Fixed workload
512 × 512 JPEG
Output ceiling: 64 tokens
Temperature 0, top_p 1
5 warmups, 30 measured requests
Baseline runtime profile
Input 1024, KV 2048, batch 1
Encoder cache: 0 bytes
Text context reuse: Off
At most 5 candidates. Stop after 3 consecutive non-improvements.
Require at least 5% lower p50 latency or peak memory, with no greater than 5% regression in the counterpart or p95 latency. Reject errors, OOM and swapping.
Notes: Warmups remain separate from measured requests. TTFT starts at request dispatch and ends on the first nonempty text delta. Completion token counts must come from real backend usage. Equivalent-quality qualification is an overlay referencing unchanged raw measurements.
Measured values supplied by output/final-findings-data.json.
Sources:
research/benchmark-method.md
GOAL.md
results/benchmark-fp16-qualified.jsonl
results/raw/benchmark-fp16-reference-01.jsonl
results/optimization-quality-policy.json
results/optimization-search-plan.json

## Slide 8
Measured FP16 baseline
Measured findings, 2026-09-20
8
Latency | p50 | p95
First visible text | 266.3 ms | 271.7 ms
Complete answer | 1830.4 ms | 1834.9 ms
20.21 tokens/s
End-to-end throughput
37 completion tokens
Shared RAM unavailable peak: 6.38 GiB
Process RSS peak: 5.90 GiB
Errors: 0 OOM: No Swap activity: No
Notes: The qualification overlay references the original 35-request run, rather than recording a second measurement. Original raw SHA256: 3ecce48f18c461161a99368c221dc87abc43a8cb1e1a7c1b199f46f8d7d65417. Shared unavailable memory equals MemTotal minus MemAvailable. RSS is the process resident set. These overlapping counters must never be added.
Measured values supplied by output/final-findings-data.json.
Sources:
results/benchmark-fp16-qualified.jsonl
results/raw/benchmark-fp16-reference-01.jsonl
results/optimization-quality-policy.json

## Slide 9
Original CPU INT4 conversion
Measured findings, 2026-09-20
9
2.22 GiB
Checkpoint file on disk
169 language linear modules
Group size 128
Native INT4 V1 kernels
First trial: all language linears
Uncalibrated RTN quantizes language linear weights and the LM head. Vision, projector and embedding tensors stay FP16.
GPTQ-compatible storage
The storage layout lets the pinned builder load RTN values. It makes no claim of GPTQ or AWQ optimization.
Checkpoint size is distinct from measured resident RAM, allocation and latency.
Notes: Group-128 symmetric round-to-nearest with stored FP16 scales and signed values -7 through 7. RTN_GPTQ dispatch describes RTN values in GPTQ-compatible packing. No GPTQ optimization, AWQ optimization, calibration dataset, GPU conversion or community checkpoint was used. Source shards stayed read-only. The exact public parser and V1/V2 repackers passed CPU tests.
Measured values supplied by output/final-findings-data.json.
Sources:
results/rtn-cpu-validation.json
scripts/quantize_cosmos3_rtn.py
scripts/rtn_backend.py
tests/test_rtn_quantization.py
https://github.com/NVIDIA/TensorRT-Edge-LLM/blob/e8b29522938901f6df19ebeedd4b69bc8edbcd97/experimental/builder/weight_packing/int4.py
https://github.com/NVIDIA/TensorRT-Edge-LLM/blob/e8b29522938901f6df19ebeedd4b69bc8edbcd97/experimental/builder/core/quantization.py

## Slide 10
Baseline, first INT4 trial and selection
Measured findings, 2026-09-20
10
Metric | FP16 baseline | First RTN: rejected | Final selected
TTFT p50 / p95 | 266.3 ms / 271.7 ms | 266.7 ms / 269.6 ms | 265.5 ms / 267.4 ms
Answer p50 / p95 | 1830.4 ms / 1834.9 ms | 1228.8 ms / 1234.2 ms | 1825.9 ms / 1830.0 ms
Shared RAM peak¹ | 6.38 GiB | 4.20 GiB | 6.43 GiB
Strict quality facts | 18/19 | 13/19 | 18/19
Reference equivalence | Pass | Fail | Pass
Selected: fp16-corrected-i1024-kv2048
¹ System RAM unavailable. Quality rejection takes precedence over latency or memory gains.
Notes: First INT4 execution status: rejected. 13/19 facts; new errors and token-limit truncation.. Selection: fp16-corrected-i1024-kv2048. Identical workload fingerprints and memory counters are required for comparisons. The selected column is a separate final verification after swap was disabled; search-trial measurements remain unchanged. Rejected RTN measurements describe a tradeoff and cannot qualify it for selection. Strict quality and reference-equivalent quality remain separate.
Measured values supplied by output/final-findings-data.json.
Sources:
results/benchmark-fp16-qualified.jsonl
results/raw/benchmark-rtn-v1-rejected-01.jsonl
results/raw/benchmark-final-service-01.jsonl
results/optimization-quality-policy.json

## Slide 11
Bounded search and memory constraints
Measured findings, 2026-09-20
11
Candidate | Result | Facts | p50 answer | RAM peak¹
FP16 reference | Selected | 18/19 | 1830.4 ms | 6.38 GiB
RTN INT4 all linears | Rejected | 13/19 | 1228.8 ms | 4.20 GiB
RTN INT4 MLP only | Rejected | 18/19 | 1026.6 ms | 5.01 GiB
FP16 fixed clocks | Rejected | 18/19 | 1758.3 ms | 6.35 GiB
Linux exposes 7.37 GiB shared physical RAM. Selected process RSS peak: 5.91 GiB.
¹ MemTotal − MemAvailable overlaps process RSS. Never add them.
CUDA allocator telemetry: not collected. Disk sizes measure storage.
Notes: Orin Nano uses unified physical RAM for CPU and GPU. MemTotal minus MemAvailable includes CPU, GPU and system pressure. Process RSS and CUDA allocator telemetry answer different questions and overlap. Disk checkpoint/engine size is separate from memory. Missing allocator telemetry is explicitly unavailable.
Measured values supplied by output/final-findings-data.json.
Sources:
GOAL.md
research/fp16-build-memory.md
results/benchmark-fp16-qualified.jsonl
results/raw/benchmark-rtn-v1-rejected-01.jsonl
results/raw/benchmark-final-service-01.jsonl
results/optimization-search-plan.json
results/benchmark-fp16-qualified.jsonl
results/raw/benchmark-rtn-v1-rejected-01.jsonl
results/raw/benchmark-rtn-mlp-rejected-01.jsonl
results/raw/benchmark-fp16-clocks-01.jsonl

## Slide 12
Selected configuration and sustained run
Measured findings, 2026-09-20
12
fp16-corrected-i1024-kv2048
FP16 preserves reference quality. Both INT4 variants add errors; fixed clocks miss the 5% gain and swap gate.
FP16 · dynamic stock 25 W · swap disabled
FP16 retained. Final service verification is separate from the four search trials.
Sustained-run check | Observed result
Duration and successful requests | 601 seconds / 366 requests
Minimum MemAvailable | 0.94 GiB
Errors / OOM / swap | 0 / No / No
Candidates considered: 4. Stop reason: Stopped after three consecutive non-improvements.
Notes: This is a bounded observed selection, not a claim of a global optimum. Final export requires a 10-minute soak, no errors/OOM/swapping, at least 512 MiB minimum MemAvailable, and explicit candidate selection. Compare latency/memory improvement only under the same declared memory counter and workload.
Measured values supplied by output/final-findings-data.json.
Sources:
results/optimization-selection.json
results/raw/benchmark-final-service-01.jsonl
results/raw/soak-final-service-01.summary.json
GOAL.md
results/optimization-search-plan.json

## Slide 13
Upstream contributions and licenses
Measured findings, 2026-09-20
13
Project / team | Contribution | Terms
NVIDIA Cosmos3-Edge | Pretrained model and tokenizer | OpenMDW-1.1
TensorRT Edge-LLM | Runtime, builders and kernels | Apache-2.0
live-vlm-webui contributors | Public interaction reference | Apache-2.0
PyTorch / Transformers | Official-model reference execution | Component licenses
Original task integration | UI, transport, repairs, measurements, RTN | Apache-2.0
Public repository contributors
UI: tokk-nv, chitoku
Runtime: nvluxiaoz, ever-wong, jhalabi-nv, nvxingkaiz, JCalafato, poweiw
Notes: Repository contributors are public contribution credits, not assigned individual ownership of each feature. NVIDIA owns the model/runtime contributions. Original task code is Apache-2.0. Model OpenMDW-1.1, JetPack/CUDA/TensorRT terms and bundled dependency licenses remain separate. Paramiko LGPL-2.1 supports the optional SSH bridge. NumPy uses BSD-3-Clause and Pillow MIT-CMU. Official PyTorch and Transformers supply reference execution. PyTorch wheels retain all bundled license notices, beyond its main BSD-style license. See the contribution ledger for exact public evidence.
Measured values supplied by output/final-findings-data.json.
Sources:
research/contribution-ledger.md
THIRD_PARTY_NOTICES.md
https://huggingface.co/nvidia/Cosmos3-Edge/blob/344d602b128d1bbdacb43b08d0a3626f46343e29/README.md
https://github.com/NVIDIA/TensorRT-Edge-LLM/blob/e8b29522938901f6df19ebeedd4b69bc8edbcd97/LICENSE
https://github.com/NVIDIA-AI-IOT/live-vlm-webui
https://github.com/huggingface/transformers/blob/c587bc884db2c2e31fc2b8102314656b17aa07b1/LICENSE
https://github.com/pytorch/pytorch/blob/cf30153c4c131c8164ee7798e5022d810682e2cb/LICENSE
https://github.com/NVIDIA/TensorRT-Edge-LLM/commit/e8b29522938901f6df19ebeedd4b69bc8edbcd97

## Slide 14
Limits and reproduction
Measured findings, 2026-09-20
14
Quality: 18/19 synthetic facts; natural photos 5/9 with partial credit, 0/3 fully correct.
Streaming checks passed. Natural-video and temporal understanding remain untested.
Small inputs are padded around a documented position-interpolation limit.
RAM and RSS overlap. CUDA allocator peak was not collected.
NVMe timeouts recur at cold load. Service recovers; storage issue remains unresolved.
Build selected engines
Native runtime + engine build:
docs/backend-build.md
Section 4, selected FP16
Serve on the Orin
sudo systemctl start cosmos-edge-backend cosmos-edge-ui
Repeat the measured workload
scripts/benchmark.py
Invocation and fixed settings:
research/benchmark-method.md
Notes: Commands are supplied from the selected validated deployment. Exact source/model revisions, conversion receipts, patch hashes, engine receipts and raw benchmark files preserve provenance. The source corpus contains public code and original task assets only. No personal-namespace project or internal repository was used.
Measured values supplied by output/final-findings-data.json.
Sources:
docs/backend-build.md
sources.lock.json
docs/quality-workload.md
patches/cosmos3-half-pixel-position.md

## Slide 15
Original goal and agent stopping policy
Measured findings, 2026-09-20
15
User-defined goal
Install JetPack through USB-C.
Run Cosmos3-Edge with TRT-Edge-LLM.
Serve streaming vision on the Orin.
Measure memory and latency.
Present findings and public-source credits.
“so you don’t keep iterating on marginal gains”
User request for a finite search
Agent-chosen policy | Recorded limit
Search ceiling | 12 initially, then 5
Each measured trial | 5 warmups + 30 requests
Required gain | At least 5%, with quality checks
Early stop | 3 consecutive non-improvements
Actual outcome | 4 trials, corrected FP16 retained
Notes: The user requested installing JetPack over USB-C, Cosmos3-Edge through TensorRT-Edge-LLM, a streaming UI served on the Orin, low memory and latency after signs of life, and a findings presentation. The user explicitly required public code and prohibited personal-namespace/internal repositories and communications. Exact user quote: “Give yourself a proper goal setting so you don’t keep iterating on marginal gains for either.” Numeric thresholds were agent choices. The initial ceiling was 12 candidates, later tightened to 5. Each measured trial used 5 warmups and 30 measured requests. Three consecutive non-improvements stop the search. A candidate needs at least 5% improvement in p50 answer latency or sampled peak memory, no greater than 5% regression in the counterpart or p95 latency, preserved reference-equivalent quality, and no errors, OOM or workload swap. Four trials were evaluated. The compact fifth trial was not run.
Safe transcript excerpts and attribution audit: research/first-version-journey.md.
Sources:
GOAL.md
results/deployment-status.json
results/optimization-search-plan.json
results/optimization-selection.json

## Slide 16
User steering and progress oversight
Measured findings, 2026-09-20
16
Progress oversight
“Did you install jetpack via the usb-c?”
“what have you done thus far?”
Connectivity reports from the user
“can you work on wifi or do you want ethernet”
“giving the GPU ethernet back and you on wifi”
Optional GPU access
“Isolate your work from anything else on that computer.”
Agent authentication failed. No remote workspace or auxiliary GPU use.
Notes: Exact user oversight prompts: “Did you install jetpack via the usb-c?” and “what have you done thus far?” These are status requests, not physical interventions. Exact connectivity reports: “Do you need the GPU? I took the ethernet offline so you can go faster, can you work on wifi or do you want ethernet”; “nvm we’ll take all night if you need to, giving the GPU ethernet back and you on wifi”. These statements are user reports, not independently verified interface changes or measured network speed improvements. Optional GPU authorization required all remote work to remain in one newly created task directory. The safe exact excerpt “Isolate your work from anything else on that computer.” omits host and credentials. The user also said “ok was able to ssh in from the terminal inside this codex side chat”. A user login did not establish agent authentication: the recorded agent clients were rejected, no task directory or files were created, and the auxiliary GPU was never used. Local Mac MPS reference execution and actual Orin GPU inference are distinct from that unused auxiliary machine.
Safe transcript excerpts and attribution audit: research/first-version-journey.md.
Sources:
GOAL.md
results/aux-gpu-status.json
results/normal-boot.json

## Slide 17
Human readiness and verified agent actions
Measured findings, 2026-09-20
17
Stage | Human report or request | Verified agent action
Recovery entry | FC REC–GND reported “done”: readiness confirmation | Detect APX, read EEPROM, upload RAM recovery
USB access | Accessory approval requested if a prompt appeared Approval unconfirmed | Use native USB SSH and an NFS bridge Complete official QSPI/NVMe flash
Normal boot | “the jumper isn’t in” Reported state, no action timestamp | Verify NVMe boot and task-key SSH Run CUDA and expand storage
Agent preparation continued while hardware readiness was unresolved.
Notes: The user reported “Poll the USB and see if you see it now, it’s jumpered FC REC and GND”. The later “done” followed a requested fresh recovery power cycle and is recorded here as a readiness confirmation, not independent proof of a detailed unplug/replug sequence or its timing. The status receipt records a user-confirmed physical reset, and the subsequent EEPROM/bulk-upload receipt passed. The user later said “the jumper isn’t in”. This establishes user-reported state, not who removed it or when. At RAM boot the agent asked for accessory approval if a prompt appeared. Approval itself was not confirmed; the agent instead verified native Mac USB SSH and used an SSH/NFS bridge around the VM networking issue. The official flash finished without reboot. The agent continued source/model and package preparation while normal-boot readiness remained unresolved. Package installation in a native ARM chroot was not GPU execution. After the user’s jumper-state confirmation, normal NVMe boot, task-key SSH, CUDA execution and storage expansion passed. Receipt timestamps are recording times. This history does not establish a physical reboot after the later systemd service installation.
Safe transcript excerpts and attribution audit: research/first-version-journey.md.
Sources:
results/host-inventory.json
results/deployment-status.json
results/jetson-board.json
results/ram-recovery-boot.json
results/usb-transfer-path.json
results/jetpack-flash-status.json
results/chroot-compute-provisioning.json
results/blocked-audit.json
results/normal-boot.json
results/cuda-preflight.json
results/final-service-audit.json

## Slide 18
First-version boundary and later follow-ups
Measured findings, 2026-09-20
18
First version: Orin inference, four trials and the soak. Benchmark ceiling stays 64 tokens.
After the first version | Current status
CPU / GPU / memory UI | Added and verified. RAM is shared system memory.
Upstream prompt + token limit | Matched the sample prompt and 512-token UI default.
Direct Orin webpage | http://192.168.6.252:8090 HTTPS: https://192.168.6.252:8443 (self-signed)
Capture defaults question | Current: 1 s minimum / 512px longest side. Upstream: 30 frames / ideal 1280×720. Unmatched.
Camera HTTPS requires accepting the local certificate warning.
Notes: Slides 1–14 preserve the first completed findings presentation and its benchmark data. First-version acceptance covered USB-C installation, real Orin inference/UI, four-trial bounded search, 600.701-second API soak, and disclosed quality/storage limits. The benchmark ceiling remains 64 output tokens. Later exact user requests: “add the cpu, gpu, and vram usage to the UI.”; “Set the max tokens and the sample prompt to the same default parameters as Web VLM UI.”; “Serve the webpage directly on the orin please”. Telemetry and default prompt/max tokens passed later browser checks. The prompt is “Describe what you see in this image in one sentence.” with max_tokens 512. Reported RAM is MemTotal minus MemAvailable on shared CPU/GPU memory, not dedicated CUDA allocator usage. The later question “Are the capture interval and the frame longest side the same defaults as Web VLM UI?” was informational, not a request to change them. Current app remains at a 1-second minimum capture interval and 512px longest side; upstream uses 30 captured frames between inference attempts and an ideal 1280×720 camera request. These are different semantics and remain unmatched. Direct LAN access is a later deployment update. Browser tests completed real image inference over both direct HTTP and HTTPS. The backend PID remained unchanged. HTTPS tests explicitly ignored certificate errors only inside their isolated browser context, verified a secure context, and exercised a synthetic camera. They do not prove a physical camera works. HTTP permits image uploads; browser camera requires a secure/trusted context. The HTTPS endpoint uses a local self-signed certificate, so browser trust is still a user setup step.
Safe transcript excerpts and attribution audit: research/first-version-journey.md.
Sources:
results/final-presentation.json
results/raw/benchmark-final-service-01.jsonl
results/raw/soak-final-service-01.summary.json
results/ui-telemetry-validation.json
results/browser-ui-telemetry.json
results/browser-ui-lan.json
web/index.html
web/app.js
https://github.com/NVIDIA-AI-IOT/live-vlm-webui/blob/2fd5ba0b334c334d24bf0f9439d8742b243d22be/src/live_vlm_webui/vlm_service.py#L42
https://github.com/NVIDIA-AI-IOT/live-vlm-webui/blob/2fd5ba0b334c334d24bf0f9439d8742b243d22be/src/live_vlm_webui/video_processor.py
https://github.com/NVIDIA-AI-IOT/live-vlm-webui/blob/2fd5ba0b334c334d24bf0f9439d8742b243d22be/src/live_vlm_webui/static/index.html#L2329
https://github.com/NVIDIA-AI-IOT/live-vlm-webui/blob/2fd5ba0b334c334d24bf0f9439d8742b243d22be/src/live_vlm_webui/static/index.html#L2659
results/ui-lan-deployment.json